## Slide 1: Covidien Gateway Prototype With RS232
January 3, 2012
By Shahid N. Shah

## Slide 2: Architecture Covidien Gateway with RS232
MEDICAL
DEVICE
MEDICAL
DEVICE
Data Generator
EXTERNAL DEVICE
(Concentrator)
PUBLISHER
PUBLISHER
PUBLISHER
PUBLISHER
MEDICAL
DEVICE
SUBSCRIBER
SUBSCRIBER
SUBSCRIBER
SUBSCRIBER
DDS
DDS
Serial port to Serial port
Serial port To USB
Serial port to ethernet [TCP/UDP]

## Slide 3: Legacy device to Gateway (direct)
Serial Port to Serial Port Communication:
  Requirements are RS232 cable and the library file
    The library files should be included on the source code to make communication between two serial ports.
    Some of the libraries available for the serial to serial communication
        Termios - C library
        Libserial - C++ library
        Boost.ASIO-++ Boost Library
MEDICAL
DEVICE
PUBLISHER
RS232 CABLE

## Slide 4: Legacy device to Gateway (direct)
Serial Port to Ethernet:
    Serial to Ethernet need a external device to convert the serial data to TCP/UDP packets. There is many devices available for this. Some of the devices given below
      http://www.perle.com/products/Serial-to-thernet.shtm
      http://aaxeon.com/Products/Serial%20to%20Ethernet.html
      Data will be retrieved through a usual socket program between the External device and publisher. In the external device we receive the serial data and converted into the TCP/UDP packets.
          Note : Wireless external device also has same process
MEDICAL
DEVICE
EXTERNAL DEVICE
(Concentrator)
PUBLISHER
ETHERNET
RS232 CABLE

## Slide 5: Legacy device to Gateway (direct)
Serial Port to USB :
    Serial to USB need a serial to USB adapter to convert the serial data to USB. There is many adapters available for this. Some of the adaptors given below
      http://www.digi.com/products/usb/anywhereusb
      http://www.fugawi.com/web/products/hardware_usb_cable.html
        In this case we need to use own code to retrieve the USB data. Based on the USB protocol we have to write code. Otherwise we need to use some of the third party libraries.
MEDICAL
DEVICE
PUBLISHER
SER IAL TO USB ADAPTER

## Slide 6: Legacy device data format to DDS
Command Line options for# ./<device>-serial-pub
    Available options for are:
      --help Produce help message
      --device-path Device path ex: /dev/tty1So1
                (Used for Serial-to-Serial and Serial-to-USB)
      --data-gen-ip arg Data Generator IP (Converter IP)
      --data-gen-port arg Data Generator Port (Configured port)
      --domain arg Device Domain
      --device-id arg Device ID - for device identification
      --log-info arg Log Info Specification
      --log-data arg Log Data Specification
      --log4cpp-conf arg Log Configuration and Format specification file

## Slide 7: Legacy device data format to DDS
There is no difference in the subscriber side for Serial port based publishers
./serial-sub {command line options}
  Available options for
      --help Produce help message
      --domain Device Domain
      --device-id Device ID - for device identification
      --log-info arg Log Info Specification
      --log-data arg Log data Specification
      --log4cpp-conf arg Log Configration and Format specification file

## Slide 8: Requirements in Serial Port
IDL type definition
Type of data format is received
Physical connection between the devices