## Slide 1: Firmware Update Proposal
Mar 06, 2012
By Shahid N. Shah

## Slide 2: Firmware Update
Medical device gateway checking repository update on regular basis in Covidien HQ.
If update found, download the update and storing it in the web store of the medical device gateway(web store means update with internal URL).
Medical device gateway publishing firmware update in the DDS topic “FIRMWARE_UPDATE”
struct FirmwareUpdate
{
string deviceDomain;
string deviceID;
string URL;
int versionMajor;
int versionMinor;
int version;
bool fullUpdate;
}
Medical devices always listening DDS topic “FIRMWARE_UPDATE”. If the deviceDomain and deviceID matches, then using the URL - device will update their firmware.

## Slide 3: Firmware Update Multiple Devices
Sometimes update should be for one particular domain devices.
Example:
deviceDomain: BP
deviceID: common
In this case the all the devices under the BP should be updated.
Sometimes update should be for all the devices.
Example:
deviceDomain: common
deviceID: common
In this case the all the devices should be updated.

## Slide 4: Firmware Update Flow
Covidien HQ
And
Firmware Repository
Medical Device Gateway
Checking for Repository
Update on Regular Basis
Pulling Firmware Update
From Repository
Web Store
Storing Pulled Update in Web store

## Slide 5: Firmware Update Flow
Medical Device Gateway
DDS TOPIC
“FIRMWARE_UPDATE”
PUBLISHING
FIRMWARE UPDATE
BP Devices
Web Store
PULSEOX Devices
ECG Devices
Devices Listening for Updates
If Update found, using the URL and devices update their firmware
Legacy Devices
PC/LAPTOP
Devices
Using Yellowdog for Firmware update

## Slide 6: Questions