## Slide 1: Covidien Gateway Prototype Project Status and Plan
October 18, 2011
By Shahid N. Shah

## Slide 2: Gateway prototype project overview
Define and design general technical approach
Architectural Design and Planning
  Define all major components of the architecture
  Research available open-source solutions for each of the major components
  Perform due diligence on each open source solution based on stability, support, and long-term maintenance capabilities
  Install all major architectural components and subsystems as a proof of concept
  Create a benchmarking, testing and quality assurance strategy/plan
  Create or run code to conduct benchmarking of major architectural components
  Create scalability test approach

## Slide 3: Common Design Requirements
Alerting and annunciation
Device / system reliability and general monitoring
Device communication
Patient acuity reports
Pushing data to other systems
Capturing data from other systems
Display multiple of same parameter
Tunable sampling rates
ADT interface
Tie into hospital IT security
 Courtesy of Dr. Chris Carnes

## Slide 4: Ensure testability and validation
Encourage reusable testing and validation
  Create system abstractions (simulations, etc.)
  Create component abstractions (devices, etc.)
Focus on data-oriented test scenarios
Create data generators, loggers, and initiators for test scenarios
Encourage automated testing from day 1
Start using and building simulators for ecosystem validation

## Slide 5: Next Gen Gateway Architecture
Web Application Stack
On-Premise Appliance or Cloud Deployment
Data Integration Stack
Content Management System
Data Services and Persistence Stack
Relational Database
Taxonomy
Full Text Search
Biz Intel
Secure, HIPAA-Compliant, Web Server
Reporting
Dashboards
Alerting
Enterprise Service Bus
Analytics
Data Mining
OLAP
Notifications
Process Mgmt
Integration
ETL
Gateway
EII
Metadata
Rules Engine
Secure, MU- and HIPAA-Compliant, Clinical Data Repository (CDR) and Master Patient Index (MPI)
HL7
X.12
IM / E-mail
Themes
App Store
Forms
Documents
EHR Modules
Security & Auditing
CCR
Patient Manager
Secure Messaging
Social Networks
HCP Directories
Target multiple devices like PC, SmartPhone, Tablet, Voice
HIE/NHIN Integration
EHR Integration
NLP & Patterns
Med Device Integration
Single sign on (LDAP, SAML)
Mobility Stack
Med Device Tethering
HIPAA Encryption & RBAC
Provisioning & Auditing
Legacy App Connectivity
Graph DB (RDF)
Content Repository
LDAP
 As defined by Netspective Medigy Platform
DDS

## Slide 6: Gateway prototype connectivity
OMG Data Distribution Service for Real-Time Systems (DDS)
Custom REST or SOAP Web Services
Advanced Message Queuing Protocol (AMQP)
Extensible Messaging and Presence Protocol (XMPP)
Simple Network Management Protocol (SNMP)
Minimal Lower Layer Protocol (MLLP) with HL7
Wireless Communication Transfer Protocol (WCTP)
IEEE 11073 (x73)
X.12 over TCP/IP

## Slide 7: The prototype’s components
Real Device (test data)
Gateway Prototype (Virtual Machine)
Simulated Corporate Cloud
Simulated Network
Simulated Hospital Systems
Simulated Device (test data)
Wired
DDS
DDS
REST
HL7
X.12

## Slide 8: Assuming real-time protocol requirement
Non-realtime (millisecond resolution with best-effort delivery)
Non-deterministic
Use at server
Use in the cloud
Realtime (microsecond resolution with guarantees)
Deterministic
Use at server
Use in the cloud
Use inside devices

## Slide 9: Assuming publish / subscribe
Hub/Spoke – high coupling
Gateway Alarm Handler, Data Store
Device
Device
EHR / HIS
Remote UI
Publish/Subscribe – low coupling
Gateway
Med Device
Med Device
Data Store
EHR / HIS
Remote UI
Alarm Handler
Cloud / EHR / HIS
Supports one-to-one, one-to-many, many-to-one, and many-to-many communications
iOS
Android
PC App
Mobile App
Any others
Independent DB
Server or
Phone

## Slide 10: Technical Deliverables
Gateway platform as virtual machine
Simulation data generator (test data)
Simulation commands controller
Simulation data publisher for pulse ox (“pulseox”), blood pressure (“bp”), and temperature (“temp”) data
Real data listeners and event handlers that respond to either actual device or simulated data
  Echo data to console
  Echo data to web page (graphs)
  Complex event processing
  Persistence

## Slide 11: Schedule Overview
' 11
Sep 2011
Oct
Nov
Dec
Jan 2012
Feb
' 12
Today
Executive Review
2/1/12
Engineering Review
1/1/12
Create test plan
12/1/11
Scalability evaluation
12/1/11
Benchmarking & evaluation
11/15/11
Design review
11/1/11
Define persistence strategy
10/24/11
Choose IDLs
10/14/11
Finalize technical approach
10/1/11
Build VM
9/12/11
Start Design
9/1/11
Refine
1/1/12
2/1/12
Test
12/1/11
1/1/12
Build
11/1/11
12/1/11
Design
10/1/11
11/1/11
Define
9/1/11
10/1/11

## Slide 12: Prototype base platform
VMware Server 4.1 ESXi Hypervisor
VMware Virtual Machine (“the gateway”)
Ubuntu 10 64bit
OpenSplice HDE Release V5.4 (DDS)
Simd-cxx – v0.9 (DDS framework)
Boost Library (messaging framework)
MongoDB v2.0 (database)
Mongo cxx driver v1.8 (database driver)

## Slide 13: Simulated messages IDL
struct DeviceStatus
{
string deviceDomain;
string deviceId;
string deviceStatus;
}
struct BloodPressure
{
string deviceDomain;
string deviceID;
long timeOfMeasurement;
short systolicPressure;
short diastolicPressure;
short pulseRatePerMinute;
}
struct PulseOximeter
{
string deviceDomain;
string deviceID;
long timeOfMeasurement;
short SPO2;
short pulseRatePerMinute;
}
struct Temperature
{
string deviceDomain;
string deviceID;
long timeOfMeasurement;
short temp;
}

## Slide 14: Simulation data generator
Generates the random data for Pulse-ox, Blood Pressure and temperature as per the structure defined in the previous slide.
Has some pre-defined constraints to generate random data. (example systolic random data between 1 to 210 mmHg)
Simultaneously creates timestamp for each data that is generated.
Multithreaded process because so that it can handle multiple processes in a given time interval.

## Slide 15: Simulation commands controller
Accept commands and start running the appropriate publisher.
Commands Controller
COMMAND : BLOOD_PRESSURE
  BP PUBLISHER
PARTITION : DEVICE_BP
TOPIC : BP
START
RUNNING

## Slide 16: Simulation data publisher
  PULSEOX PUBLISHER
  BP PUBLISHER
  TEMP PUBLISHER
PARTITION : DEVICE_PULSEOX
TOPIC : PULSEOX
PARTITION : DEVICE_BP
TOPIC : BPECHO
PARTITION : DEVICE_TEMP
TOPIC : TEMPECHO

## Slide 17: Simulated data publisher
Started by the commands controller
Communicates with data generators and publishes the data to subscribers
TEST DATA GENERATOR
BP
PUBLISHER
DDS
COMMAND DETAILS
GENERATED DATA
PUBLISHING DATA

## Slide 18: Simulation data event handlers
  PULSEOX_ECHO
PARTITION : DEVICE_PULSEOX
TOPIC : PULSEOX_ECHO
  PULSEOX_ANALYSIS
PARTITION : DEVICE_PULSEOX
TOPIC : PULSEOX_AVG
  PULSEOX_ALARM
PARTITION : DEVICE_PULSEOX
TOPIC : PULSEOX_ALARM
  BP_ECHO
PARTITION : DEVICE_BP
TOPIC : BP_ECHO
  TEMP_ECHO
PARTITION : DEVICE_TEMP
TOPIC : TEMP_ECHO
  BP_ALARM
PARTITION : DEVICE_BP
TOPIC: BP_ALARM
  TEMP_ANALYSIS
PARTITION : DEVICE_TEMP
TOPIC: TEMP_AVG
  TEMP_ALARM
PARTITION : DEVICE_TEMP
TOPIC: TEMP_ALARM

## Slide 19: Simulation data event handlers
Get the publishers written data to DDS and displays that data.
No storing process is done here.
DDS
BP_ALARM
LISTENER
LISTENER PULLS
DATA FROM DDS
Pulls sequence of blood pressures, check the constraints for alarm and displays

## Slide 20: Simulation data persistence
Persistence Listeners will get data from TOPIC and store the data
No processing will be done

## Slide 21: Simulation data persistence
Same as the listeners mentioned in the previous slide, but stores the gathered data to database. No other processes done here.
DDS
BP_ALARM
PERSISTENCE LISTENER
LISTENER PULLS
DATA FROM DDS
DATABASE
STORES IN
MONGODB

## Slide 22: Data flow summary
TEST DATA GENERATOR
COMMANDS CONTROLLER
IT GETS THE COMMAND AND STARTS APPROPRIATE PUBLISHER
PUBLISHER
SEND THE COMMAND DETAILS
DDS
SENDS THE GENERATED DATA
PUBLISHER WRITES THE DATA COLLECTED FROM DATA GENERATOR
LISTENER
PERSISTENCE LISTENER
DATABASE
PULLING DATA FROM DDS
PULLING DATA FROM DDS
ECHO/DISPLAY OR ANALYZE THE DATA
STORE THE DATA IN DATABASE

## Slide 23: Gateway prototype “first principles”
Focus all attention on data interoperability, test beds, simulators, risk assessment, and physiologic evaluation tools first
  Look at tools like ECGSyn (at physionet.org)
Focus attention on general software architecture, languages, tools, etc. second
Specify a “zero tolerance” policy to prevent creation of new software when open source software exists (or commercial software to some extent if it doesn’t create a success tax)

## Slide 24: Need help with device inventory
Inventory all devices
Inventory all sensors within devices
Create directory of data generated by sensors in devices
For each sensor, create an IDL (“table” or “data type”) file using 11073 nomenclature
For each sensor, fill out data types (“fields”) based on 11073 DIM
Map directory of data to IEEE 11073 DIM and nomenclature
Focus on data spec, you’re creating a central data model for all sensor data
Define DDS domain structure
Define DDS topics tied to specific data types

## Slide 25: Questions